MRB-BD42 / MRB-BD4X v3 User Manual
# Features
- Four extremely sensitive (12-15k ohms) independent channels
- Easy per-channel sensitivity adjustment
- Isolated detection to prevent coupling track power and signal systems
- Simple installation doesn't require cutting track power wires
- Open source MRBus interface (MRB-BD42 version only)
- Expansion ports for up to two extra MRB-BD4X on every MRB-BD42 for up to 8 extra channels
- Four easy-to-use logic level outputs (5V @ 15mA maximum, MRB-BD4X version only)
# Applications
- Block detection for signaling systems
- Activate grade crossing signals
- Monitor train progress in hidden areas
- Simulating a spring switch using an MRServo switch machine
# Differences between MRB-BD42 vs MRB-BD4X
MRB-BD42 detectors are designed to integrate with MRBus, an open source model railroad control bus based on RS-485 and promoted by Iowa Scaled Engineering. For more information, see http://www.mrbus.org
MRB-BD4X detectors are designed to provide four 5V logic level outputs, each corresponding to one channel of the detector. These can be used independently, connected to your own signal logic, or as expansion modules for a MRB-BD42.
# Operation
The MRB-BD42/BD4X are four-channel current-based model railroad block occupancy detectors for DCC layouts. They require the alternating DCC signal to operate reliably, and will either not work or work erratically with most DC layouts.
The BD42/BD4X use current transformers – the large black tombstone-shaped items on the board – to sense small amounts of current used by DCC decoders and cars with resistor-equipped wheelsets. As such, they are electrically isolated from track power, preventing damaging currents from find stray paths between your boosters and your expensive signal gear.
# Using the MRB-BD4X Outputs
The MRB-BD4X has four logic-level outputs. Outputs will be high (5V) upon detection and low (0V) when not detecting. Never expose these outputs to a voltage outside that range, or draw more than 20 milliamps from them. To switch higher currents or voltages, please use something like our ACC-RELAY1 module.
Do not exceed 20mA on any output, or short any output pin to 5V, GND, or any other voltage. Damage to the block detector will likely result.
# Using the MRB-BD42 Auxilliary Inputs
The MRB-BD42 comes with two 6p6c connectors that provide regulated +5VDC, GND, and four 5V logic level inputs. These can be used to connect additional MRB-BD4X expanders to have up to 12 block detection channels, or can be used for auxiliary digital inputs. Never exceed 5VDC on any of the input pins and do not draw more than 150mA from the 5V line if using them as auxiliary digital inputs from your own modules.
# Installation
Securely mount the MRB-BD42/BD4X to the model railroad benchwork using the four mounting holes provided. When choosing a mounting location, make sure nothing conductive will contact the back of the circuit board, as this may cause short circuits, malfunctions, and permanent damage.
### Powering the Detector
Both versions of the detector need a power supply to operate.
The MRB-BD42 requires 8-16VDC applied to the VIN and GND terminals. Typically this will be the MRBus power pair. The MRBus data pair should be connected to the A/B terminals, same as any MRBus node.
The MRB-BD4X can be fed from either 8-16VDC applied to the VIN and GND terminals, same as the BD42, or can be fed clean, regulated 5VDC through the 5V/GND terminals near the logic level ouputs.
Do not exceed 5V if feeding power through the 5V power supply input terminal. Power fed in through this terminal is neither regulated nor filtered, and exceeding 5V will cause the immediate destruction of the module.
### Wiring Blocks For Detection
For each block to be detected, gap at least one rail at each end of the block. Connect all the feeder wires for the gapped rail to a common bus wire, and run that wire through the center of the current transformer on the BD42/BD4X.
Only a single pass through the transformer is recommended, but for sensing very small currents, the wire can be looped through twice.
Note 1: DCC circuit breakers and auto-reversers draw a minute (but variable) amount of current, and will trigger the block detectors. Any breakers or reversing modules should be installed between the DCC booster and the BD42/BD4X, not between the detector and the track.
Note 2: For neatness and to minimize cross-talk between blocks, it's recommended to zip tie the two halves of the wire above the current transformer.
### Setting the Sensitivity
Contrary to popular belief, an empty track block does not always draw zero current. Because of resistive leakage through scenery (including wooden ties in varying humidity) and capacitive effects between the rails and feeder wires, there's often a very small leakage current.
The MRB-BD42/BD4X has an adjustment potentiometer (pot) on each channel to allow you to tune out this leakage current. Rotating the potentiometer clockwise will increase the sensitivity (detects occupancy at lower currents) and counter-clockwise will decrease sensitivity.
To tune each channel:
1) Turn on your DCC system and make sure no equipment is in the block.
2) If the red “detect” LED is on for the channel you're working on, you can skip this step. Otherwise, use a small flathead screwdriver to slowly turn the potentiometer clockwise until the red light just comes on.
3) Now turn the pot counter-clockwise slowly until the LED turns off. At this point, your channel is calibrated.
4) While not typical, it is possible that changes to the layout – humidity, temperature, ballasting the track, etc. - can change the leakage current. You may need to repeat the procedure if you get false occupancy in the future.

# Configuration Values
As a MRBus-based device, the MRB-BD42 has a number of configuration registers that can be used to change how the device operates.
The MRB-BD4X also uses many of these registers, but has no network through which to update them conveniently. For most applications, the default values will work without any issues. However, for more specialized applications, they can be changed from their default value using an AVR programmer.
CV	Purpose	Default	Possible Values	Description
0x00	Node Address	3	1-254	The node address for this MRB-BD42
0x02 / 0x03	Update Time H / Update Time L	20	1-65535	Interval, in 1/10ths of seconds, at which occupancy updates are sent if there is no change
0x10 / 0x11 / 0x12 / 0x13	Ch1 On Delay / Ch2 On Delay / Ch3 On Delay / Ch4 On Delay	4	1-254	Delay between when occupancy is first detected on a channel and when the module indicates occupancy. The units are roughly 1/250th of a second. Larger numbers result in longer delays.
0x20 / 0x21 / 0x22 / 0x23	Ch1 Off Delay / Ch2 Off Delay / Ch3 Off Delay / Ch4 Off Delay	25	1-254	Delay between when occupancy is no longer detected on a channel and when the module returns to not indicating occupancy. The units are roughly 1/250th of a second. Larger numbers result in longer delays.
0x30 / 0x31 / 0x32 / 0x33 / 0x34 / 0x35 / 0x36 / 0x37	Ch1 Threshold H / Ch1 Threshold L / Ch2 Threshold H / Ch2 Threshold L / Ch3 Threshold H / Ch3 Threshold L / Ch4 Threshold H / Ch4 Threshold L	65535	1-1023	Sets the threshold current for when a block is considered “detected”. If value is 65535 (default), the input from the potentiometer will be used instead for setting the detection threshold.

# Open Design
Iowa Scaled Engineering is committed to creating open designs that users are free to build, modify, adapt, improve, and share with others.
### Hardware
The design of the CKT-IRSENSE hardware is open source hardware, and is made available under the terms of the Creative Commons Attribution-Share Alike v3.0 license, a copy of which is available from: http://creativecommons.org/licenses/by-sa/3.0/
Design files can be found on the Iowa Scaled Engineering website:
http://www.iascaled.com/store/MRB-BD42
http://www.iascaled.com/store/MRB-BD4X
### Firmware
The official Iowa Scaled Engineering firmware for the MRB-BD42 and MRB-BD4X is free software: you can redistribute it and/or modify it under the terms of the GNU General Public License as published by the Free Software Foundation, either version 3 of the License, or (at your option) any later version. A copy of the GNU GPL can be found at: http://www.gnu.org/licenses/gpl.html
New firmware can be flashed into the MRB-BD42/MRB-BD4X through J1. The six pin connectors is a standard AVR 6-pin ISP header.

Iowa Scaled Engineering
http://www.iascaled.com/ support@iascaled.com